## Slide 1
SRI RAMAKRISHNA ENGINEERING COLLEGE
Course Instructor:
Mr.R.Chandru,
Assistant Professor(Sl.G)/ECE
No. of Credits : 3
20EC214 & DIGITAL CMOS VLSI CIRCUITS
Department of Electronics and Communication Engineering
[Educational Service : SNR Sons Charitable Trust]
[Autonomous Institution, Reaccredited by NAAC with ‘A+’ Grade]
[Approved by AICTE and Permanently Affiliated to Anna University, Chennai]
[ISO 9001-2015 Certified and all eligible programmes Accredited by NBA]
VATTAMALAIPALAYAM, N.G.G.O. COLONY POST, COIMBATORE – 641 022.

## Slide 2: 20EC214 - DIGITAL CMOS VLSI CIRCUITS COURSE OUTCOMES
On successful completion of the course, students will be able to,
COURSE OUTCOMES | 
CO1 | Interpret the characteristics and manufacturing process technologyof MOS transistor.
CO2 | Analyze the various logic styles of CMOS combinational andsequential circuits
CO3 | Design the various digital arithmetic logic circuits.
CO4 | Illustrate the performance of the digital circuits by examining the timing issues.
CO5 | Make use of MOS concepts in construction of Memory Array Subsystem.

## Slide 3: 20EC214 - DIGITAL CMOS VLSI CIRCUITS COURSE CONTENTS
PREREQUISITES
20EC204 - Digital System Design
MOS TRANSISTOR AND PROCESSING 10
MOSFET theory - Transistor switches - Compound gates - Design equations - IV characteristics - CV characteristics - Second order effects - Energy and Power - Resistance Estimation - Capacitance Estimation - Switching Characteristics - RC Delay Models - Logical Effort for gates - CMOS Process technology - Design Rules and Layout.
CMOS LOGIC STRUCTURES 11
Combinational Circuits: CMOS Inverter - DC Characteristics - Complementary Logic Structures - Ratioed logic - Pass transistor logic - Transmission gate - Tristate Inverter - Multiplexers - Dynamic logic structures. Sequential Circuits: Static latches and Registers, Dynamic latches and Registers, Pulse Registers, Sense Amplifier Based Register, Pipelining.
DESIGN OF ARITHMETIC BUILDING BLOCKS 8
Full adder, Ripple carry adder, Carry bypass adder, Linear and Square root carry-select adder, Carry look-ahead adder - Multipliers - Barrel and logarithmic shifter.
TIMING ISSUES 8
Timing Basics, Sources of Skew and Jitter, Clock-Distribution Techniques, Latch-Based locking, Self-Timed Circuit Design, Synchronizers and Arbiters, Clock Synthesis and Synchronization Using a Phase-Locked Loop.
MEMORY ARRAY SUBSYSTEM 8
SRAM: SRAM Cells, Row Circuitry, Column Circuitry. Multiported SRAM and Register files DRAM: Subarray Architectures, Column Circuitry, Embedded DRAM. Read-Only Memory: Programmable ROMs, NAND ROMs, Flash.

## Slide 4: 20EC214 - DIGITAL CMOS VLSI CIRCUITS COURSE CONTENTS
TEXT BOOKS
Neil H.E. Weste and David Harris, "CMOS VLSI Design A Circuits and Systems Perspective", 4th Edition, Pearson Education, Reprint 2010.
Jan M. Rabaey, Anantha Chandrakasan and B Nikolic, "Digital Integrated Circuits: A Design Perspective", 2nd Edition, Pearson Education India, 2016.
REFERENCES
Douglas. A. Pucknell, Kamran Eshraghian, "Basic VLSI Design", 3rd Edition, Prentice Hall India, 2010.
John P.Uyemura, "Introduction to VLSI Circuits and Systems", John Wiley & Sons, 2012.
WEB REFERENCES
https://nptel.ac.in/courses/108/107/108107129/
https://nptel.ac.in/courses/117/106/117106093/

## Slide 5: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
MOSFET theory –
Transistor switches
Compound gates
Design equations - IV characteristics - CV characteristics
Second order effects
Energy and Power
Resistance Estimation
Capacitance Estimation
Switching Characteristics
RC Delay Models
Logical Effort for gates
CMOS Process technology
Design Rules and Layout

## Slide 6: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Gajski Y-Chart

## Slide 7: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Gajski Y-Chart
The Y-chart consists of three major domains, namely:
        Behavioral Domain
        Structural Domain
        Physical Domain
Physical/Geometry Domain:-
It is first necessary to subdivide a large system into small ASIC sized pieces which is referred as physical partition.
After that the small blocks are arranged together in the form of clusters.
Then the next step is floor plan where it is necessary to find out the approximate location of each module or block in the chip.
After that we can move on to module layout and cell layout where each unit of block to be placed on chip and the connections between the cells and the block is defined.

## Slide 8: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Gajski Y-Chart
Behavioral Domain:-
The behavior of the entity can be modelled using procedural code which can represent the circuit at a higher level of abstraction.
First hierarchy is system where the behavior of the architecture is defined
Then a set of algorithm needs to be defined for processing the different parameters and a set of flowchart.
The third step is RTL where the coding needs to be done and then the logic level where we are concerned with 0 and 1 level, after which the transfer function is defined.
Structural Domain:-
A particular block is connected across with set of signals or netlist and here in this case we are more interested in the structure.

## Slide 9: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
VLSI Design Flow
VLSI design cycle start with a formal specification of a VLSI chip, follows a series of steps, and eventually produces a packaged chip.

## Slide 10: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
System Specification
First step of design process is to lay down the specification of the system.
High level representation of the system.
Factors considered:
  Performance
  Functionality
  Physical dimension
  Design technique
  Fabrication technology
It is a compromise between market requirements, technological and economical viability.

## Slide 11: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Functional Design
Main functional units of the system are identified
Identifies the interconnect requirements between the units
The area, power and other parameters of each unit are estimated
The behavioral aspects of the system are considered not implementation specification
- multiplication needed but does not specify its hardware
The key idea is to specify behavior, in terms of
  Input
  Output
  Timing of each unit
Without specifying the internal structure.

## Slide 12: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Logic Design X = (AB+CD)(E+F) Y= (A(B+C) + Z + D)
Design the logic, that is
      Boolean expressions,
      control flow,
      word width,
      register allocation, etc.
The outcome is called an RTL (Register Transfer Level) description.
RTL is expressed in a HDL (Hardware Description Language), such as VHDL and Verilog.
This description can be used in simulation and verification.
As this description consists of Boolean expressions, so they can be minimized to achieve the smallest logic design.

## Slide 13: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Circuit Design
The purpose of the circuit design is to develop a circuit representation based on the logic design.
The Boolean expression can be converted into a circuit representation by taking into consideration the speed and power requirements of the original design.
Design the circuit including gates, transistors, interconnections, etc. The outcome is called a netlist.
Circuit simulation is used to verify the correctness and timing of component.

## Slide 14: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Physical Design
The circuit representation of each component is converted into geometric representation.
Convert the netlist into a geometric representation. The outcome is called a layout.
Connections between different components are also expressed as a geometric pattern.
Exact details depends upon design rules
It is a complex process and usually broken down into sub-steps.
Various verification and validation checks are performed on the layout during physical design.

## Slide 15: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Fabrication
Fabrication Process includes,
- lithography,
    - polishing,
    - deposition,
    - diffusion, etc.,
to produce a chip.
Fabrication process consists of several steps and requires various masks.
Before the chip is mass produced, a prototype is made and tested

## Slide 16: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Packaging, Testing and Debugging
Packaging
  Put together the chips on a PCB (Printed Circuit Board) or an MCM (Multi-Chip Module)
Each chip is then packaged and tested to ensure that it meets all the design specifications and that it functions properly.

## Slide 17: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
MOS Transistors
Introduction
Silicon (Si),
A semiconductor, forms the basic starting material for most integrated circuits
Pure silicon consists of a three-dimensional lattice of atoms
Silicon is a Group IV element, so it forms covalent bonds with four adjacent atoms, as shown below

## Slide 18: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
MOS Transistors
Silicon valence electrons are involved in chemical bonds, pure silicon is a poor conductor.
The conductivity can be raised by introducing small amounts of impurities, called dopants, into the silicon lattice.
  A dopant from Group V of the periodic table, such as arsenic, has five valence electrons. It replaces a silicon atom in the lattice and still bonds to four neighbors, so the fifth valence electron is loosely bound to the arsenic atom, as shown below

## Slide 19: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
MOS Transistors
Thermal vibration of the lattice at room temperature is enough to set the electron free to move,
  leaving a positively charged As+ ion and a free electron.
  The free electron can carry current so the conductivity is higher
  this is an n-type semiconductor because the free carriers are negatively charged electrons.
Group III dopant, such as boron, has three valence electrons, as shown below,
  The dopant atom can borrow an electron from a neighboring silicon atom, which in turn becomes short by one electron.
  That atom in turn can borrow an electron, and the missing electron, or hole, can propagate about the lattice.
  The hole acts as a positive carrier, call this a p-type semiconductor.

## Slide 20: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
A junction between p-type and n-type silicon is called a diode, as show.
When the voltage on the p-type semiconductor, called the anode, is raised above the n-type cathode, the diode is forward biased and current flows.
When the anode voltage is less than or equal to the cathode voltage, the diode is reverse biased and very little current flows.
MOS Transistors

## Slide 21: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Metal-Oxide-Semiconductor (MOS) structure,
Created by superimposing several layers of conducting and insulating materials to form a sandwich-like structure.
  structures are manufactured using a series of chemical processing steps involving,
    Oxidation of the silicon,
    selective introduction of dopants,
    and deposition and etching of metal wires and contacts.
MOS Transistors

## Slide 22: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Metal-Oxide-Semiconductor (MOS) structure,
CMOS technology provides two types of transistors,
    n-type transistor (nMOS)
    p-type transistor (pMOS)
MOS Transistors
Transistor operation is controlled by electric fields so called Metal Oxide Semiconductor Field Effect Transistors (MOSFETs) or simply FETs.

## Slide 23: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Metal-Oxide-Semiconductor (MOS) structure,
Cross-sections and symbols of these transistors are shown below. The n+ and p+ regions indicate heavily doped n- or p- type silicon.
MOS Transistors
a) n-MOS b) p-MOS

## Slide 24: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Transistor consists of,
  a stack of the conducting gate
  an insulating layer of silicon dioxide (SiO2, known as glass)
  the substrate (silicon wafer)
  body, or bulk.
Gates of early transistors,
  were built from metal, the stack was called metal oxide-semiconductor or MOS.
  1970s, the gate has been formed from polycrystalline silicon (polysilicon), but the name stuck.
  metal gates reemerged in 2007, to solve materials problems in advanced manufacturing processes
MOS Transistors

## Slide 25: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
An nMOS transistor,
  is built with a p-type body
  has regions of n-type semiconductor adjacent to the gate called the source and drain.
  The body is typically grounded.
A pMOS transistor,
  is just the opposite, consisting of p-type source and drain regions with an n-type body.
MOS Transistors

## Slide 26: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
An nMOS Transistor,
The body is generally grounded so the p–n junctions of the source and drain to body are reverse-biased.
If the gate is also grounded,
  no current flows through the reverse-biased junctions, the transistor is OFF.
MOS Transistors – As a Switch
If the gate voltage is raised,
  it creates an electric field that starts to attract free electrons to the underside of the Si–SiO2 interface.
If the voltage is raised enough,
  the electrons out number the holes and a thin region under the gate called the channel is inverted to act as an n-type semiconductor.
    a conducting path of electron carriers is formed from source to drain and current can flow, the transistor is ON.

## Slide 27: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
An nMOS Transistor,
When the gate of an nMOS transistor is 0,
  the transistor is OFF and no current flows from source to drain
When the gate of an nMOS transistor is 1,
  the transistor is ON and there is a conducting path from source to drain
MOS Transistors – As a Switch

## Slide 28: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
A pMOS transistor,
The situation is again reversed. The body is held at a positive voltage.
When the gate is also at a positive voltage,
  the source and drain junctions are reverse-biased and no current flows, the transistor is OFF.
MOS Transistors – As a Switch
When the gate voltage is lowered,
  positive charges are attracted to the underside of the Si–SiO2 interface.
A sufficiently low gate voltage,
  inverts the channel and a conducting path of positive carriers is formed from source to drain, the transistor is ON.

## Slide 29: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
A pMOS transistor,
When the gate of an pMOS transistor is 0,
  the transistor is ON and there is a conducting path from source to drain
When the gate of an pMOS transistor is 1,
  the transistor is OFF and no current flows from source to drain
Notice : The symbol for the pMOS transistor has a bubble on the gate, indicating that the transistor behavior is the opposite of the nMOS.
MOS Transistors – As a Switch

## Slide 30: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
nMOS transistor:
  majority carriers are electrons(greater mobility)
  p-substrate doped (positively doped)
pMOS transistor:
  majority carriers are holes (lessmobility),
  n-substrate (negatively doped)
Mode of operation depends on Vg, Vg, Vs
MOS Transistors – Theory & Terminal Voltages
Vgs = Vg – Vs
Vgd = Vg – Vd
Vds = Vd – Vs = Vgs - V
Source and drain are symmetric diffusion terminals
By convention, source is terminal at lower voltage
Hence Vds  0

## Slide 31: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Simple MOS structure :
The top layer of the structure is a good conductor called the gate.
Early transistors used metal gates.
Transistor gates soon changed to use polysilicon, i.e., silicon formed from many small crystals, although metal gates are making a resurgence at 65 nm and beyond.
The middle layer is a very thin insulating film of SiO2 called the gate oxide.
The bottom layer is the doped silicon body.
The figure shows a p-type body in which the carriers are holes. The body is grounded and a voltage is applied to the gate. The gate oxide is a good insulator so almost zero current flows from the gate to the body.
MOS Transistors – Theory

## Slide 32: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
nMOS Transistors - Operating Modes
Gate Biasing :
Vgs=0:
no current flows from source to drain (insulated by two reverse biased pn junctions
Vgs>0:
electric field created across substrate
Electrons accumulate under gate: region changes from p-type to n-type
  Conduction path between source and drain
Enhancement - mode transistor: Conducts when gate bias Vgs > Vt
Depletion - mode transistor: Conducts when gate bias is zero

## Slide 33: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
nMOS Transistors - Operating Modes
Accumulation Mode: Figure (a)
A negative voltage is applied to the gate, so there is negative charge on the gate.
The mobile positively charged holes are attracted to the region beneath the gate. This is called the accumulation mode.
Depletion Mode : Figure (b)
A small positive voltage is applied to the gate, resulting in some positive charge on the gate.
The holes in the body are repelled from the region directly beneath the gate, resulting in a depletion region forming below the gate.

## Slide 34: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
nMOS Transistors - Operating Modes
Inversion Mode: Figure (c)
A higher positive potential exceeding acritical threshold voltage Vt is applied, attracting more positive charge to the gate.
The holes are repelled further and some free electrons in the body are attracted to the region beneath the gate. This conductive layer of electrons in the p-type body is called the inversion layer

## Slide 35: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Three regions of operation
  Cutoff
  Linear
  Saturation
nMOS Transistors – Regions of Operation
The transistor consists of the MOS stack between two n-type regions called the source and drain.
In the above Figure,
The gate-to-source voltage Vgs is less than the threshold voltage Vt
  The source and drain have free electrons
  The body has free holes but no free electrons
If the source is grounded,
  The junctions between the body and the source or drain are zero-biased or reverse-biased, little or no current flows, the transistor is OFF, and this mode of operation is called cutoff.

## Slide 36: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
In first figure,
the gate voltage is greater than the threshold voltage
an inversion region of electrons (majority carriers) called the channel connects the source and drain, creating a conductive path and turning the transistor ON.
The number of carriers and the conductivity increases with the gate voltage. The potential difference between drain and source is
there is no electric field tending to push current from drain to source.
nMOS Transistors –
Regions of Operation

## Slide 37: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
In Second figure,
When a small positive potential Vds is applied to the drain
  current Ids flows through the channel from drain to source.
  This mode of operation is termed linear, resistive, triode, non-saturate or unsaturated
  The current increases with both the drain voltageand gate voltage
nMOS Transistors – Regions of Operation

## Slide 38: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
If Vds becomes sufficiently large that Vgd < Vt ,
  the channel is no longer inverted near the drain and becomes pinched off
  Conduction is still brought about by the drift of electrons under the influence of the positive drain voltage.
  As electrons reach the end of the channel, they are injected into the depletion region near the drain and accelerated toward the drain.
  Above this drain voltage the current Ids is controlled only by the gate voltage and ceases to be influenced by the drain. This mode is called saturation.
nMOS Transistors – Regions of Operation

## Slide 39: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Summary:
The nMOS transistor has three modes of operation
If Vgs < Vt ,
  the transistor is cutoff (OFF).
If Vgs > Vt ,
  the transistor turns ON.
If Vds is small,
  the transistor acts as a linear resistor in which the current flow is proportional to Vds.
If Vgs > Vt and Vds is large,
  the transistor acts as a current source in which the current flow becomes independent of Vds .
nMOS Transistors – Regions of Operation

## Slide 40: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
pMOS transistor,
Operates in just the opposite fashion to nMOS transistor
The n-type body is tied to a high potential so the junctions with the p-type source and drain are normally reverse-biased.
When the gate is also at a high potential,
  no current flows between drain and source
When the gate voltage is lowered by a threshold Vt ,
  holes are attracted to form a p-type channel immediately beneath the gate, allowing current to flow between drain and source
pMOS Transistors – Operation

## Slide 41: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
pMOS Transistors – Operation
Vgs >> Vt : Transistor OFF
    Majority carrier in channel (electrons)
    No current from source to drain
0 > Vgs >Vt : Depletion region
    Electric field repels majority carriers (electrons)
    Depletion region forms - no carriers in channel
    No current flows (except for leakage current)
Vgs < Vt , VDS=0: Transistor ON
Electric field attracts minority carriers (holes)
Inversion region forms in channel
Depletion layer insulates channel from substrate
Current can now flow from source to drain!

## Slide 42: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
pMOS Transistors – Operation
Vgs <Vt , VDS >VGS -VT :Linear (Active) mode
  Combined electric fields shift channel and depletion region
  Current flow dependent on VGS, VDS
Vgs < Vt , VDS <VGS -VT :Saturation mode
  Channel “pinched off”
  Current still flows due to hole drift
  Current flow dependent on VGS

## Slide 43: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
MOS Device Design Equation – I V Characteristics
MOS transistors have three regions of operation:
      Cut-off or subthreshold region
      Linear region
      Saturation region
To derive a model relating the current and voltage(I-V) for an nMOS transistor in each of these regions.
The model assumes that,
  the channel length is long enough that the electric field (the field between source and drain) is relatively low
  This model is variously known as the long-channel, ideal, first-order, or Shockley model.

## Slide 44: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY

## Slide 45: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY

## Slide 46: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY

## Slide 47: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Veffective​ = gate voltage seen by the channel

## Slide 48: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Electron drift velocity:
Drain current is:

## Slide 49: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY

## Slide 50: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY

## Slide 51: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY

## Slide 52: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY

## Slide 53: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY

## Slide 54: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY

## Slide 55: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
MOS Device Design Equation - I V Characteristics
The long-channel model assumes,
  the current through an OFF transistor is 0.
When a transistor turns ON, (Vgs > Vt),
  the gate attracts carriers (electrons) to form a channel
  the electrons drift from source to drain at a rate proportional to the electric field between these regions.
  We can compute currents if we know the amount of charge in the channel and the rate at which it moves
The charge on each plate of a capacitor is
Q = CV

## Slide 56: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
MOS Device Design Equation - I V Characteristics
The charge in the channel Qchannel is,
where,
Cg, is the capacitance of the gate to the channel
(Vgc – Vt), is the amount of voltage attracting charge to the channel beyond the minimum required to invert from p to n.
The gate voltage is referenced to the channel, which is not grounded
If the source is at Vs and the drain is at Vd , the average is
Vc = (Vs + Vd)/2 = Vs + Vds /2

## Slide 57: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
MOS Device Design Equation - I V Characteristics
The mean difference between the gate and channel potentials Vgc is,
Vg – Vc = Vgs – Vds /2

## Slide 58: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Model the gate as a parallel plate capacitor with capacitance proportional to area over thickness.
If the gate has length L and width W and the oxide thickness is tox, as shown in the figure the capacitance is,
MOS Device Design Equation - I V Characteristics

## Slide 59: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
MOS Device Design Equation - I V Characteristics
term is called Cox, the capacitance per unit area of the gate oxide
is the permittivity of free space, 8.85 × 10–14 F/cm
the permittivity of SiO2 is kox = 3.9 times as great
Gate Dielectric with a higher dielectric constant,
  tox is called the equivalent oxide thickness (EOT)
The thickness of a layer of SiO2 , that has the same Cox
  tox is thinner than the actual dielectric

## Slide 60: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Each carrier in the channel,
  is accelerated to an average velocity, v, proportional to the lateral electric field,
  i.e., the field between source and drain.
The constant of proportionality µ is called the mobility
v = µE
A typical value of µ for electrons in an nMOS transistor with low electric fields is 500–700 cm2/V· s.
The electric field E is the voltage difference between drain and source Vds divided by the channel length
MOS Device Design Equation - I V Characteristics

## Slide 61: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
The time required for carriers to cross the channel is the channel length divided by the carrier velocity: L/v
The current between source and drain is the total amount of charge in the channel divided by the time required to cross
MOS Device Design Equation- I V Characteristics
The term Vgs – Vt arises so often that it is convenient to abbreviate it as VGT
The geometry and technology-dependent parameters are some times merged into a single factor - β

## Slide 62: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
In the equation,
MOS Device Design Equation - I V Characteristics
Vgs > Vt , but Vds relatively small, It is called linear or resistive because when Vds << VGT, Ids increases almost linearly with Vds, just like an ideal resistor.

## Slide 63: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
In the equation,
MOS Device Design Equation - I V Characteristics
If Vds > Vdsat = VGT, the channel is no longer inverted in the vicinity of the drain, say it is pinched off.
Beyond this point, called the drain saturation voltage, increasing the drain voltage has no further effect on current.
Substituting, Vds = Vdsat at this point of maximum current into above equation, the expression for the saturation current that is independent of Vds.

## Slide 64: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
The above expression is valid for Vgs > Vt and Vds > Vdsat
  Thus, long-channel MOS transistors are said to exhibit square-law behavior in saturation.
Two key figures of merit for a transistor are Ion and Ioff.
  Ion (also called Idsat) is the ON current, Ids
      When, Vgs = Vds = VDD.
  Ioff is the OFF current
      when Vgs = 0 and Vds = VDD
According to the long-channel model,
Ioff = 0 and
MOS Device Design Equation - I V Characteristics

## Slide 65: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
The current in the three regions :
MOS Device Design Equation - I V Characteristics

## Slide 66: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
MOS Device Design Equation - I V Characteristics
nMOS I-V characteristics of ideal 4/2 λ
THE FIRST-ORDER MODEL,
The current is zero for gate voltages below Vt
For higher gate voltages,
  Current increases linearly with Vds for small Vds
As Vds reaches the saturation point
Vdsat = VGT
  Current rolls off and eventually becomes independent of Vds when the transistor is saturated.
THE SHOCKLEY MODEL,
Over estimates current at high voltage because it does not account for mobility degradation and velocity saturation caused by the high electric fields.

## Slide 67: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
pMOS transistors behave in the same way, but with the signs of all voltages and currents reversed.
The I-V characteristics are in the third quadrant
The current flows from source to drain in a pMOS transistor.
The mobility of holes in silicon is typically lower than that of electrons.
This means that pMOS transistors provide less current than nMOS transistors of comparable size and hence are slower.
MOS Device Design Equation - I V Characteristics
pMOS I-V characteristics of ideal 4/2 λ

## Slide 68: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
  Threshold Voltage
  Body Effect
  Sub-Threshold Region
  Channel-Length Modulation
  Mobility Variation
  Fowler-Nordheim Tunneling
  Drain Punch through
  Impact Ionization-Hot electrons

## Slide 69: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Body Effect
The threshold voltage VT​ of a MOSFET increases when the source is at a higher potential than the substrate (body).
The body effect is a second-order effect in MOSFETs where the threshold voltage increases when there is a voltage difference between the source and substrate. As the source-to-body voltage increases, the reverse bias of the source–body junction increases, widening the depletion region and increasing the depletion charge. To maintain charge neutrality, the inversion charge must reduce, requiring a higher gate voltage to form the channel. This results in an increase in threshold voltage.

## Slide 70: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Body Effect
In arranging the devices to form gating functions it might be necessary to connect several devices in series
The Effect of substrate bias on series connected n-transistor
This results in an increase in source to substrate voltage, as vertically along series chain ( Vsb1=0, Vsb2 ≠ 0)
Under normal Conditions, When Vgs > Vt,
  the depletion layer width remains constant and charge carriers are pulled into the channel from the source

## Slide 71: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Body Effect
As the substrate bias Vsb (Vsource – V substrate) is increased,
  the width of the channel substrate depletion layer also increases, resulting in an increase in the density of the trapped carriers in the depletion layer.
For charge neutrality to hold,
  The channel charge must decrease
The result effect is the substrate voltage Vsb adds to the channel substrate junction potential
  This increase the gate channel voltage drop
  The overall effect is the increase of threshold voltage Vt(Vt2>Vt1)

## Slide 72: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Body Effect
Vsb affects the charge required to invert the channel
– Increasing Vs or decreasing Vb increases Vt
s = surface potential at threshold
- Depends on doping level NA
– And intrinsic carrier concentration ni
 = body effect coefficient

## Slide 73: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY

## Slide 74: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Sub-Threshold Region
The cut off region is also referred to as the sub- threshold region
  Where,
  Ids, increases exponentially with Vds and Vgs
The value of Ids is very small,
  the finite value of Ids may be used as advantage to construct very low power circuits, or
  it may adversely affect circuits such as dynamic charge storage nodes

## Slide 75: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Gate-Induced Drain Leakage
Occurs at overlap between gate and drain
  when drain is at VDD, gate is at a negative voltage
  Stops efforts to reduce subthreshold leakage using a negative gate voltage

## Slide 76: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Channel-Length Modulation
The behavior of an MOS device assumes that the carrier mobility is constant
And does not take into account the variation in channel length due to the changes in drain to source voltages Vds
For long channel length,
  The influence of channel variation is of little
When a MOS device is in saturation,
  The effective channel length is,

## Slide 77: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
The reduction in channel length increases the (W/L) ratio, there by increases β as the drain voltage increase.
The MOS device rather appearing as a constant current source with infinite output impedance it has a finite output impedance
The above behavior is represented by,
Channel-Length Modulation

## Slide 78: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Gate Voltage and the Channel
Channel-Length Modulation

## Slide 79: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
The Mobility ‘µ’ describes the ease with which carries drift in the substrate material. It is defined by,
If the velocity V is given by cm/sec, the electric field E in v/cm, the mobility has the dimensions cm2/v-sec
Mobility vary in number of ways
  Negative charge carriers in silicon have much higher mobility than positive charge carriers
  Decreases with increasing doping concentration and increasing temperature
  Temperature variations becomes less pronounced as the doping density increases
Mobility Variation

## Slide 80: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
When gate oxide is very thin a current can flow from the gate to source or drain by electron tunneling through the gate oxide.
Current is proportional to the area of the gate of the transistor.
Where,
  Eox is the electric field across the gate oxide and Eo and C1 are constants.
  Eox = Vgs/Tox
  – This effect limits the thickness of the gate oxide as processes are scaled.
Fowler-Nordheim Tunneling

## Slide 81: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
When the drain voltage is high with respect to source, the depletion region around the drain may extend to source, causing current to flow irrespective of gate voltage.
Drain Punch Through
Electric field from drain affects channel
More pronounced in small transistors where the drain is closer to the channel
Drain-Induced Barrier Lowering
  Drain voltage also affect Vt
  Vt  Vt Vds
High drain voltage causes current to increase

## Slide 82: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
As the length of the gate of a MOS transistor is reduced, the electric field at the drain of a transistor in saturation increases
For submicron gate lengths,
  The field can become so high that electrons are imparted with enough energy to become HOT.
  i.e. reaching a critical high level of energy, under intense electric field which occurs when the channel is short (saturation)
These hot electronics impact the drain, dislodging holes that are then swept towards the negatively charged substrate and appears as a substrate current
  This effect is known as Impact Ionization
Impact Ionization

## Slide 83: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
The electrons can penetrate the gate oxide, causing a gate current
  This lead to degradation of the MOS device parameters
  Which in turn can lead to the failure of circuits
While the substrate current may be used in a positive manner to estimate the severity of the Hot Electrons Effect, it can lead to poor refresh times in,
        Dynamic Memories
        Noise in Mixed Signals
        Possibility latch up
Hot Holes do not normally present a problem because of their lower mobility
Impact Ionization

## Slide 84: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Modeling can be defined as,
“The method of finding the parameter values for fixed simulator model equations”
MOS modeling -Writing a set of equations that link voltages and currents
Behavior of the device can be simulated and predicted
Basic MOS model components
  Equations describing Ids (Vds) and Ids (Vgs)
  Parameters that link the technology being used for fabrication
MOS Modelling

## Slide 85: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Requirements of Good MOS Model
Good I-V characteristic accuracy
Meet charge conservation requirement
Correct values of small-signal quantities
Good prediction for white and 1/f noise
Ability to provide results even when device operation is quasi static
Ability to include all physical mechanisms for sub- micron devices

## Slide 86: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY

## Slide 87: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
MOS Parameters

## Slide 88: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Small Signal AC Characteristics
The MOS transistor can be represented by the simplified (Vsb=0) small signal equivalent model as shown below,

## Slide 89: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
The MOS transistor is modeled as a voltage – controlled current source (gm), output conductance (gds), the interelectrode capacitance.
The output conductance (gds), in the linear region can be obtained by differentiating,
With respect to Vds, results in an output drain,
* Vds, must be small compared
to Vgs for the MOS device to be
in a linear region
Small Signal AC Characteristics

## Slide 90: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
The channel resistance Rc is approximated by,
Rc,
  it is controlled by the gate to source voltage
  it valid for gate to source voltage that maintain constant mobility in the channel
In saturation, [Vds ≥ (Vgs – Vt)], the MOS device behaves like a current source, the current being almost independent of Vds, this is verified by,
Small Signal AC Characteristics

## Slide 91: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Due to some channel shortening the drain current characteristics have some slope, This slope defines the gds of the transistor
The output conductance can be decreased by lengthening the channel (L)
The transconductance gm express the relationship between output current, Ids and the input voltage Vgs,
  It is used to measure the gain of the MOS device
Small Signal AC Characteristics

## Slide 92: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
In the linear region gm is given by,
In the Saturation region gm is given by,
Transconductance must have a positive value, the absolute value is used for voltages applied to p-type devices.
Small Signal AC Characteristics

## Slide 93: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Each terminal of an MOS transistor has capacitance to the other terminals.
  these capacitances are nonlinear and voltage dependent (C-V)
They can be approximated as simple capacitors ,
  when their behavior is averaged across the switching voltages of a logic gate
  simple models of each capacitance suitable for estimating delay and power consumption of transistors
  used for circuit simulation
C-V CHARACTERISTICS OF MOS TRANSISTORS

## Slide 94: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Simple MOS Capacitance Models
The gate of an MOS transistor is a good capacitor.
Its capacitance is necessary to attract charge to invert the channel, so high gate capacitance is required to obtain high Ids.
The gate capacitor can be viewed as a parallel plate capacitor with the gate on top and channel on bottom with the thin oxide dielectric between.
  The capacitance is,
C-V CHARACTERISTICS OF MOS TRANSISTORS

## Slide 95: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Simple MOS Capacitance Models
The bottom plate of the capacitor is the channel, which is not one of the transistor’s terminals.
When the transistor is on, the channel extends from the source (and reaches the drain if the transistor is unsaturated, or stops short in saturation).
  the gate capacitance as terminating at the source and call the capacitance Cgs
Transistors used in logic are of minimum manufacturable length results in,
        greatest speed and
        lowest dynamic power consumption
C-V CHARACTERISTICS OF MOS TRANSISTORS

## Slide 96: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Simple MOS Capacitance Models
Taking this minimum L as a constant for a particular process, we define,
where,
If a more advanced manufacturing process is developed, in which both the channel length and oxide thickness are reduced by the same factor, Cpermicron remains unchanged
C-V CHARACTERISTICS OF MOS TRANSISTORS

## Slide 97: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Simple MOS Capacitance Models
Addition to the gate, the source and drain also have capacitances.
  These capacitances are not fundamental to operation of the devices, but do impact circuit performance and are called Parasitic Capacitors
  The source and drain capacitances arise from the p–n junctions between the source or drain diffusion and the body and are called Diffusion Capacitance, Csb and Cdb .
C-V CHARACTERISTICS OF MOS TRANSISTORS

## Slide 98: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Simple MOS Capacitance Models
A depletion region with no free carriers forms along the junction.
  The depletion region acts as an insulator between the conducting p- and n-type regions, creating capacitance across the junction.
  The capacitance of these junctions depends on,
    the area
    perimeter of the source and drain diffusion
    the depth of the diffusion
    the doping levels
    and the voltage
  As diffusion has both high capacitance and high resistance, it is generally made as small as possible in the layout.
C-V CHARACTERISTICS OF MOS TRANSISTORS

## Slide 99: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Simple MOS Capacitance Models
Three types of diffusion regions are frequently seen, illustrated by the two series transistors,
  (a) Isolated Diffusion
  (b) Shared Diffusion
  (c) Merged Diffusion
C-V CHARACTERISTICS OF MOS TRANSISTORS
Diffusion Region Geometries

## Slide 100: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Simple MOS Capacitance Models
C-V CHARACTERISTICS OF MOS TRANSISTORS
Each source and drain has its own isolated region of contacted diffusion
The drain of the bottom transistor and source of the top transistor form a shared contacted diffusion region.
The source and drain are merged into an uncontacted region.
The average capacitance of each of these types of regions can be calculated or measured from simulation as a transistor switches between VDD and GND.

## Slide 101: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Simple MOS Capacitance Models
Manual Estimation,
  can observe that the diffusion capacitance Csb and Cdb of contacted source and drain regions is comparable to the gate capacitance
    Example: 1–2 fF/µm of gate width
  The diffusion capacitance of the uncontacted source or drain is somewhat less because the area is smaller but the difference is usually unimportant
    Values of Cg = Csb = Cdb ≈ 1 fF/µm will be used
C-V CHARACTERISTICS OF MOS TRANSISTORS

## Slide 102: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
MOS Gate Capacitance Model
The MOS gate sits above the channel and may partially overlap the source and drain diffusion areas.
  The gate capacitance has two components:
      The intrinsic capacitance Cgc (over the channel)
      The overlap capacitances Cgol (to the source and drain)
The intrinsic capacitance was approximated as a simple parallel plate in,
with capacitance, C0 = WLCox
The bottom plate of the capacitor depends on the mode of operation of the transistor
C-V CHARACTERISTICS OF MOS TRANSISTORS

## Slide 103: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
MOS Gate Capacitance Model
The intrinsic capacitance has three components representing the different terminals connected to the bottom plate,
  # Cgb (gate-to-body) # Cgs (gate-to-source) # Cgd (gate-to-drain)
C-V CHARACTERISTICS OF MOS TRANSISTORS
Capacitance vs. Vds in the linear and saturation regions
Capacitance vs. Vgs in the cutoff region and for small Vds
Intrinsic Gate Capacitance :
Cgc = Cgs + Cgd + Cgb as a function of
(a) Vgs and (b) Vds

## Slide 104: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
C-V CHARACTERISTICS OF MOS TRANSISTORS
MOS Gate Capacitance Model
Cutoff Region :
When the transistor is OFF (Vgs < Vt),
  the channel is not inverted and charge on the gate is matched with opposite charge from the body. This is called Cgb, the gate-to-body capacitance
For negative Vgs,
  the transistor is in accumulation and Cgb = C0
  As Vgs increases but remains below a threshold, a depletion region forms at the surface.
  This effectively moves the bottom plate downward from the oxide, reducing the capacitance, as shown in the plot.
Capacitance vs. Vgs in the cutoff region and for small Vds

## Slide 105: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
C-V CHARACTERISTICS OF MOS TRANSISTORS
MOS Gate Capacitance Model
Linear Region :
When Vgs > Vt,
  the channel inverts and again serves as a good conductive bottom plate.
  the channel is connected to the source and drain, rather than the body, so Cgb drops to 0
At low values of Vds,
  the channel charge is roughly shared between source and drain, so Cgs = Cgd = C0/2
As Vds increases,
  the region near the drain becomes less inverted, so a greater fraction of the capacitance is attributed to the source and a smaller fraction to the drain, as shown in the plot
Capacitance vs. Vds in the linear and saturation regions

## Slide 106: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
C-V CHARACTERISTICS OF MOS TRANSISTORS
MOS Gate Capacitance Model
Saturation Region :
At Vds > Vdsat,
  the transistor saturates and the channel pinches off.
  At this point, all the intrinsic capacitance is to the source, as shown in the plot, because of pinch-off, the capacitance in saturation reduces to Cgs = 2/3 C0 for an ideal transistor
Capacitance vs. Vds in the linear and saturation regions

## Slide 107: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
C-V CHARACTERISTICS OF MOS TRANSISTORS
MOS Gate Capacitance Model
The behavior in the three regions can be approximated as shown in Table below.
Approximation for Intrinsic MOS Gate Capacitance

## Slide 108: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
C-V CHARACTERISTICS OF MOS TRANSISTORS
MOS Gate Capacitance Model
Note :
It is convenient to view the gate capacitance as a single-terminal capacitor attached to the gate (with the other side not switching).
As, the source and drain actually form second terminals, the effective gate capacitance varies with the switching activity of the source and drain.
More accurate modeling of the gate capacitance may be achieved by using a charge based model.
For the purpose of delay calculation of digital circuits, we usually approximate,
or use an effective capacitance extracted from simulation
Shows the effective gate capacitance in a 0.35µm process for seven different combinations of source and drain behavior
Fig. Data-dependent Gate Capacitance

## Slide 109: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
C-V CHARACTERISTICS OF MOS TRANSISTORS
MOS Gate Capacitance Model
The gate overlaps the source and drain in a real device and also has fringing fields terminating on the source and drain.
This leads to additional overlap capacitances, These capacitances are proportional to the width of the transistor.
Typical values are,
Cgsol = Cgdol = 0.2 – 0.4 fF/µm
They should be added to the intrinsic gate capacitance to find the total.
Overlap Capacitance

## Slide 110: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
MOS Diffusion Capacitance Model
The p–n junction between the source diffusion and the body contributes parasitic capacitance across the depletion region.
The capacitance depends on both the area AS and sidewall perimeter PS of the source diffusion region.
The area is AS = WD
The perimeter is PS = 2W +2D
Of this perimeter,
W abuts (adjacent to)the channel
and the remaining,
W + 2D does not
The total source parasitic capacitance is,
C-V CHARACTERISTICS OF MOS TRANSISTORS

## Slide 111: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
MOS Diffusion Capacitance Model
The total source parasitic capacitance is,
Where,
Cjbs , the capacitance of the junction between the body and the bottom of the source having units of capacitance/area
Cjbssw, the capacitance of the junction between the body and the side walls of the source having units of capacitance/length
C-V CHARACTERISTICS OF MOS TRANSISTORS

## Slide 112: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
MOS Diffusion Capacitance Model
As, the depletion region thickness depends on the bias conditions, these parasitics are nonlinear.
The area junction capacitance term is,
Where,
CJ is the junction capacitance at zero bias and is highly process dependent.
MJ is the junction grading coefficient, typically in the range of 0.5 to 0.33 depending on the abruptness of the diffusion junction.
Ψ0 is the built-in potential that depends on doping levels
C-V CHARACTERISTICS OF MOS TRANSISTORS

## Slide 113: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
MOS Diffusion Capacitance Model
The area junction capacitance term is,
Ψ0 is the built-in potential that depends on doping levels
Where,
  vT , is the thermal voltage from thermodynamics, not to be confused with the threshold voltage Vt . It has a value equal to kT/q (26 mV at room temperature)
where ,
k = 1.380 ×10–23 J/K is Boltzmann’s constant
T, is absolute temperature (300 K at room temperature)
q = 1.602 × 10–19 C is the charge of an electron
  NA and ND , are the doping levels of the body and source diffusion region
  ni, is the intrinsic carrier concentration in undoped silicon and has a value of 1.45 × 1010 cm–3 at 300 K
C-V CHARACTERISTICS OF MOS TRANSISTORS

## Slide 114: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
C-V CHARACTERISTICS OF MOS TRANSISTORS
MOS Diffusion Capacitance Model
The sidewall capacitance term is of a similar form but uses different coefficients
In processes below about 0.35µm that employ shallow trench isolation surrounding transistors with an SiO2 insulator,
  the sidewall capacitance along the nonconductive trench tends to be minimal, while the sidewall facing the channel is more significant
  SPICE models, the capacitance of this sidewall abutting the gate and channel is specified with another set of parameters:

## Slide 115: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
MOS Diffusion Capacitance Model
Diffusion regions were historically,
  used for short wires called runners in processes with only one or two metal levels
Diffusion capacitance and resistance are large enough that such practice is now discouraged,
  diffusion regions should be kept as small as possible on nodes that switch
C-V CHARACTERISTICS OF MOS TRANSISTORS
MOS transistor can be viewed as,
a four-terminal device with capacitances between each terminal pairs
The gate capacitance includes an intrinsic component (to the body, source and drain, or source alone, depending on operating regime) and overlap terms with the source and drain.
The source and drain have parasitic diffusion capacitance to the body.
Capacitance of an MOS Transistor

## Slide 116: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Compound Gates
A compound gate performing a more complex logic function in a single stage of logic is formed by using a combination of series and parallel switch structures.
FOR EXAMPLE,
The derivation of the circuit for the function
is shown in Figure, (Next Slide)
CMOS LOGIC

## Slide 117: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Compound Gates
FOR EXAMPLE, The derivation of the circuit for the function
CMOS LOGIC
This function is sometimes called AND-OR-INVERT-22, or AOI22 because it performs the NOR of a pair of 2-input ANDs.

## Slide 118: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Compound Gates
Fig (a) Shows, For the nMOS pull-down network,
  take the un-inverted expression ((A · B) + (C · D)) indicating when the output should be pulled to ‘0.’
  The AND expressions (A · B) and (C · D) may be implemented by series connections of switches
Fig (b) Shows,
  Now ORing the result requires the parallel connection of these two structures
CMOS LOGIC

## Slide 119: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Compound Gates
Fig (c) & (d) Shows, For the pMOS pull-up network,
  compute the complementary expression using switches that turn on with inverted polarity.
  By DeMorgan’s Law, this is equivalent to interchanging AND and OR operations.
From now,
  Transistors that appear in series in the pull-down network must appear in parallel in the pull-up network.
  Transistors that appear in parallel in the pulldown network must appear in series in the pull-up network.
  This principle is called conduction complements and has already been used in the design of the NAND and NOR gates.
CMOS LOGIC

## Slide 120: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY
Compound Gates
Fig (c) & (d) Shows, In the pull-up network,
  the parallel combination of A and B is placed in series with the parallel combination of C and D.
CMOS LOGIC
Fig (e) Shows,
  Putting the networks together yields the full schematic
Fig (f) Shows,
  The symbol of the function is shown is shown

## Slide 121: MODULE 1 MOS TRANSISTOR AND PROCESSING TECHNOLOGY